## Slide 1: Human-Robot Interaction for Object Transfer
Luís Almeida
Master's Dissertation in Mechanical Engineering
Supervisors:
Prof. Vítor Manuel Ferreira dos Santos
Prof. Filipe Miguel Teixeira Pereira da Silva
Aveiro, 13 December 2016

## Slide 2: Overview
1
2
3
4
5
6
Introduction
Experimental Setup
Robot Control
Pre-contact Approximation using 3D Vision
Contact and Force-based Interaction
Conclusions and Future Work

## Slide 3
Context and Motivation;
Problem Formulation;
Dissertation Goals.
Overview
1
Introduction

## Slide 4: Introduction – Context and Motivation
PR2
Domo
1
“The HRI problem is to understand and shape the interactions between one or more humans
and one or more robots”
Physical human-robot interaction
Provide physical assistance to a worker on an assembly line;
Extend the time an elderly person can live at home;
Help with household chores.
“Robots are designed and built to complement human abilities”

## Slide 5: Introduction – Problem Formulation
The robot control to perform the inherent movements of the transfer assignment;
The human-robot pre interaction;
The interaction by contact.
1

## Slide 6: Introduction – Dissertation goals
Hardware and software infrastructure installation and familiarization;
Study of management mechanisms of pre-contact approximation using 3D vision;
Study and development of interaction mechanisms by contact.
1

## Slide 7
Hardware;
Software.
Overview
2
Experimental Setup

## Slide 8: Experimental Setup – Hardware
Cyton Gamma 1500 Manipulator
Kinect
ATI Mini40 Transducer
Force-Sensitive Resistor (FSR)
2
7 DOF
Kinematically redundant

## Slide 9: Experimental Setup – Software
Robot Operating System (ROS);
MoveIt!;
Kinematics and Dynamics Library (KDL);
OpenNI;
2

## Slide 10: Robot Control
Overview
3
Joint Controller;
Forward Kinematics;
Inverse Kinematics;
Evaluations.

## Slide 11: Robot Control – Joint Control
ROS stack dynamixel motor - used to interface with the Robotis Dynamixel line of servo motors
Roslaunch files - used to launch and start the controll of Cyton dynamixel servos
3
dynamixel driver
dynamixel controllers
dynamixel msgs

## Slide 12: Robot Control – Foward Kinematics
Determination of end-effector position and orientation as a function of the joint angles
From the DH parameters it is possible to determinate the Cartesian position of the end-effector in terms of joint angles (, ,..., )
3

## Slide 13: Robot Control – Synchronous Movement
Being [n] = {1,2,...,7} , the velocity for each joint (ω(i)) can be calculated as expressed
by the following equations:
3
Reduce Cyton’s vibrations and overload problems
Smoother motion and precise control
 | - maximum displacement
 | - desired joint angle
 | - joint angle state
 | - time of execution
 | - pre-defined max angular velocity
 | - angular velocity
 | - displacement
 | - maximum displacement
 | - desired joint angle
 | - joint angle state
 | - time of execution
 | - pre-defined max angular velocity
 | - angular velocity
 | - displacement

## Slide 14: Robot Control – Inverse Kinematics
Inverse Kinematics (IK) is the method of determining a set of joint angles that will satisfy a given end-effector pose in the Euclidean space
MoveIt! + KDL
3
ROS package robot_model - 3D robot model
MoveIt! Setup Assistant - configuration files

## Slide 15: Robot Control – Workspace Analysis
3
Problem - Large workspace which leads to a large, not-suitable for
inverse kinematics, calculation time.
Limit the number of orientations for the end-effector
4 orientations are used to improve the interaction between robot and user
Maximum run rate 10 times better
Allow the user to make contact with the sensor, using the object, without considerable manipulation

## Slide 16: Robot Control – Reachability Analysis
3
11 random points inside Cyton workspace are used
The EE average error is approximately 1%
The accuracy of the robot control is very high

## Slide 17
Human Hand Tracking;
Kinect-Robot Frame Transformation;
Object Detection;
Evaluations.
Overview
4
Pre-contact Approximation using 3D Vision

## Slide 18: 3D Vision – Human Hand Tracking
4
The position of the hand is published as a tf transform
OpenNI tracker – allows a user to track his own skeleton using a 3D sensor
Right hand

## Slide 19
4
3D Vision – Kinect-Robot Frame Transformation
1.560 m
0.700 m
0.788 m
The workspace is within the 3D sensor field of view and nominal depth range
The layout ensures that the robotic arm does not block the human hand relatively to the sensor
Two methods to transform the Kinect frame to the robot frame:
Method 1. Done manually with a measurement tape
Method 2. Uses two point clouds; use the function ”estimateRigidTransformation”

## Slide 20
3D Vision – Colour Based Object Detection
4
HSV values are within the following range:
140 ≤ H ≤ 179
179 ≤ S ≤ 255
126 ≤ V ≤ 191
Object detection - so that robot knows when the user intends to enter in a transfer state
Colour based detection
Uses OpenCV features to handle image colour processing

## Slide 21
3D Vision – Accuracy Analysis
4
100 readings of the hand positioned on those points are recorded
3D sensor average and max error
Offset: 7cm in robot y axis

## Slide 22
3D Vision – Frame Transformation Analysis
4
A set of coordinates well known to the robot are used as the input for the transformation
Frame transformation methods comparison
Concerning the first method, the average error showed up as approximately 5.36%, on average less 1.38% when compared with the second transform approach

## Slide 23
Pre-contact Approximation using 3D Vision
4
Data was recorded 5 times daily for 10 days:
If the environment conditions don’t significantly change, this algorithm can always detect the object
Only the environment luminosity changes are considered;
Environment luminosity changes plus red objects in the environment (such as: red clothes, red figures in wallpapers and red writing material);
The HSV parameters are adapted daily.

## Slide 24
ATI mini40 integration;
FSR integration;
Evaluations.
Overview
5
Contact and Force-based Interaction

## Slide 25
Force-based Interaction – ATI mini40 Integration
5
A device to acquire the signals
Send them to a PC for conversion into forces and torques
Special components to install the sensor in the robotic arm

## Slide 26
Force-based Interaction – Signal Converter
5
Arduino plus Ethernet shield (sends a message through TCP/IP )
Arduino can only read analogue inputs within a range of 0-5V
A dedicate circuit was developed to perform signal conditioning
Operating principle of the developed circuit

## Slide 27
Force-based Interaction – Code implementation
5
Each gauge does not match a single force or torque in a single
direction, which means that each of them depends on all six gauges
=
- transpose vector of = []
- transpose vector of = [G0 G1 G2 G3 G4 G5]
Multiplying the transform matrix by a vector of gauges readings (), it is possible to find
the forces and torques values for these readings

## Slide 28
Force-based Interaction – Sensor Installation
5
Mounting side adapter
Tool side adapter
Mounting side adapter
ATI sensor
Tool side adapter

## Slide 29
Force-based Interaction – FSR Integration
5
ATI transducer got damaged throughout the work
Feel the object between gripper’s fingers
Detect the starting and ending phases of the object transference
To fulfil these needs, two FSR are installed in Cyton’s gripper
The idea is to observe FSR’s feedback and use it to dictate gripper actions

## Slide 30
Force-based Interaction – FSR Integration
5
Diagram with states and transitions modeling the objet transfer between a human and the robot

## Slide 31
Force-based Interaction – FSR’s Overall Assembly
5
The FSR’s are glued in the center of the gripper’s fingers
These are connected to a box, containing the Arduino plus shields and the voltage dividers, through flex cable
The Arduino is connected through Ethernet to the client computer
2 FSR
Flex cable
Arduino + Ethernet shield + Proto shield
2 Voltage divider

## Slide 32
Force-based Interaction - Evaluations
5
The object transfer task mainly consists of 4 objects being handed over from the user to the robot gripper
Robot arm stiffness is reduced, which affects the force propagation between the object and the sensor
The experimental tests are done with symmetric objects
Object: A B C D

## Slide 33
Force-based Interaction – Force Evolution
5
I
III
Object A
Object C
Object B
Object D

## Slide 34
Force-based Interaction – Force Evolution
5
I
III

## Slide 35
Force-based Interaction – Force Evolution
5
Force evolution for object B in a transference
Illustrations corresponding to the phases (I, II, III and IV) marked on the force evolution graphs
I
III
IV
II

## Slide 36
Force-based Interaction – Repeatability Analysis
5
the forces required to hold the objects are approximately 9, 7, 13 and 14 Newton
force differences are mainly caused by the objects different properties and geometries
a stiffer object (e.g. object A and B when compared with object C and D), requires lower force
A
B
C
D

## Slide 37
Force-based Interaction – Success Rate
5
Transfer Algorithm Success Rate
Each object is transferred 100 times in order to analyse the success rate
One successful transfer corresponds to the fulfillment of the four phases
The success rate for the objects A and B is quite good
The water bottle object is the one presenting the lower success rate
because not only its properties affect the transference, but its surface
irregularities makes the contact even more difficult

## Slide 38
Conclusions;
Future Work.
Overview
6
Conclusions and Future Work

## Slide 39
6
Conclusions
The low level control of the robotic arm is accomplished by making use of the dynamixel packages and the MoveIt! software incorporated with a kinematic and dynamic library
The pre-interaction approach using vision is successfully achieved using a 3D sensor
Concerning the interaction by contact approach, despite the misfortune occurred with the ATI sensor mini 40, the implementation of force sensitive resistors made it possible to achieve the proposed goal

## Slide 40
6
Future Work
A better robotic manipulator should be used for this kind of task
A torque/force sensor should be implemented in the wrist joint of the manipulator arm
The gripper’s fingers should have more force sensitive resistors to improve the diversity of objects that can be handed over
A complete force analysis, taking into consideration object friction and weight
A database with different objects properties, so that the 3D sensor can recognize the objects and thus adjust the gripper position, orientation and force required to hold these objects

## Slide 41: Human-Robot Interaction for Object Transfer
Luís Almeida
Thank You