Movimento(WAAS)

GLL - Geographic position, Latitude and Longitude

$GPGLL,4038.17,N,00839.51,W

4038.17,N		Latitude 40 deg. 38.17 min. North

00839.51,W		Longitude 008 deg. 39.51 min. West

VTG - Track made good and ground speed

$GPVTG,225,T,230,M,04.0,N,07.5,K

225,T		True track made good

230,M		Magnetic track made good

04.0,N		Ground speed, knots

07.5,K		Ground speed, Kilometers per hour

Parado(WAAS)

$GPGLL,4038.18,N,00839.50,W

$GPVTG,000,T,000,M,00.0,N,00.0,K